## Slide 1
User Manual
Kit to explore Autonomous
Vehicle Technology

## Slide 2
An affordable AI robot, powered by
Python and MIT App Inventor
Learning to explore
Autonomous Vehicle Technology
Introducing

## Slide 3
Introduction
What’s in the Box
AI-Lite Construction
AI-Lite Connection and Testing
Do's & Don'ts for Using AI-Lite Bot
MIT App Inventor Connection
MIT App Inventor Projects
Python Setup for AI-Lite
Python Projects
Table of Contents

## Slide 4
AI-Lite is an autonomous robot built for a variety of applications. Equipped with a sophisticated Two-wheel & four-wheel drive system, integrated camera, ultrasonic sensors, IR sensor, color sensor, and touch sensor, it excels at navigating complex environments with accuracy and intelligence. AI-Lite is ideal for tasks involving advanced obstacle detection, machine learning, and real-time monitoring, making it a powerful tool for both educational and industrial use. Python is the primary language used for executing its projects.
    Introduction
Figure - 1​

## Slide 5
Scan the QR code to watch a detailed video demonstration on:
      AI-Lite features and capabilities
      Example projects using MIT App Inventor
      Python integration for advanced projects
      Practical applications and real-world use cases
    AI-Lite Intro Video
Figure - 2​

## Slide 6
    What’s in the box?
Component | Quantity | Image
Brain block | 1 | 
Motor blocks | 4 | 
Ultrasonic & IR sensor block | 1 | 

## Slide 7
Component | Quantity | Image
Wheels | 4 | 
Camera Module Block | 1 | 
Color Sensor Module | 1 | 

## Slide 8
Component | Quantity | Image
Base Plates – 2 x 6 | 4 | 
Half Bricks – 2 x 6 | 6 | 
Half Bricks - 1 x 6 | 1 | 
Traffic Signs | 4 | 

## Slide 9
Component | Quantity | Image
Half Brick - 2 x 4 | 1 | 
Half brick 2 x 2 | 2 | 
Custom Blocks | 2 | 
Black Caster cap | 1 | 

## Slide 10
AILITE CONSTRUCTION
Follow these steps to assemble the AILITE using the provided kit :
Motor setup​
Brain Block Assembly​
Brain Block Placement​
Fixing Wheels​
Camera Module​
Ultrasonic Sensor​
Color Sensor

## Slide 11
AI-Lite Construction for Two Wheel Bot
Scan the QR code for direct access to detailed assembly instructions, component lists, and a comprehensive online manual with videos and step-by-step tutorials to simplify the construction process
Figure - 3

## Slide 12
AI-Lite Construction for Four Wheel Bot
Scan the QR code for direct access to detailed assembly instructions, component lists, and a comprehensive online manual with videos and step-by-step tutorials to simplify the construction process
Figure - 4

## Slide 13
AI-Lite Connection & Testing
Scan the below QR code to watch a detailed video demonstration on:
  Checking the connections of AI-Lite
  Understanding the significance of each color
  Setting up proper connections.
  Check its movements and sensor values
Figure - 5

## Slide 14
Do's & Don'ts for Using AI-Lite Bot
Scan this QR code to watch a video on:
  Do's and Don'ts for using the AILITE bot
  Key guidelines for optimal performance
  Common mistakes to avoid
  Tips for safe and efficient operation
  Ensuring longevity and reliability
Figure - 6

## Slide 15
MIT App Connection

## Slide 16
Install the MIT AI2 Companion App:​
  Download and install the MIT AI2 Companion app from the Google Play Store or the Apple App Store on your mobile device.​
Open MIT App Inventor:​
  Go to appinventor.mit.edu on your computer and sign in.​
Open Your Project:​
  Select the project you want to work on or create a new one.​
Click "Connect":​
  In the MIT App Inventor interface, click the "Connect" button at the top of the screen.​
Select "AI Companion":​
  From the dropdown menu, select "AI Companion."​
Open the MIT AI2 Companion App:​
  Launch the MIT AI2 Companion app on your mobile device.​

## Slide 17
7. Scan QR Code or Enter Code:​
Use your mobile device to scan the QR code displayed on your computer screen, or enter the provided code manually in the Companion app.
8. Connected:​
  Your project will now load on your mobile device, and you can test your app in real-time.​
Note:​
In MIT App Inventor, if you encounter issues with connecting and disconnecting, try the following steps on your mobile phone:​
1. Check the DHCP Settings: Access the network settings and switch from DHCP to a static IP configuration.​
2. Set a Static IP Address: Assign a static IP address to your mobile phone within the same network range.​
This can help stabilize the connection by ensuring a consistent IP address for your device.​
​
​
​

## Slide 18
MIT APP INVENTOR PROJECTS​

## Slide 19
ACCELEROMETER ​
Goal: To control the bot's direction using phone tilt motions detected by the accelerometer.​
Functionality: Detects phone tilts and sends corresponding commands to a bot.​
Key Components:​
Accelerometer Sensor: Detects the tilt of the phone.​
Real-time Processing:​
Continuously monitors the phone's accelerometer data to detect tilt movements.​
Bot Actions:​
Tilt Left: Bot turns left. Tilt Right: Bot turns right.​
Implementation Details:​
Tilt Detection:​The application uses the phone’s accelerometer to detect tilt direction.​
Software Requirements: MIT App Inventor for developing the application.

## Slide 20
FACE DETECTION :​
Goal: To control AILite's actions based on face detection.​
Functionality: Detects faces using a camera and triggers AILite to dance or spin based on the presence or absence of a face.​
Key Components:​
Personal Image Classifier: Detects faces in the camera feed.​
Real-time Processing:​
Continuously processes the camera feed to detect faces in real-time.​
Bot Actions:​
Face Detected: AILite dances. No Face Detected: AILite spins around

## Slide 21
CHATBOT​
Goal: To interact with users through yes/no questions and execute operations based on their responses.​
Functionality: Asks yes/no questions and performs actions based on the user's answers.​
Key Components:​
Question Processing: Asks and interprets yes/no questions.​
Response Handling: Provides responses and performs operations based on user answers.​
Real-time Processing:​
Continuously processes user inputs to determine and execute the appropriate operations.​
Yes: Executes a specific operation.​
No: Executes an alternative operation or provides feedback.

## Slide 22
EMOTION RECOGNITION - L1​
Goal: To recognize user emotions and trigger corresponding bot actions.​
Functionality: Detects happy or angry emotions and sends commands to a bot.​
Key Components:​
Emotion Recognition Technology: Utilizes image processing to detect facial expressions.​
Real-time Processing:​
Integrates with the device’s camera to continuously monitor and analyze the user's facial expressions in real-time.​
Bot Actions:​
Happy: Initiates a dance sequence. Angry: Moves away from the user.

## Slide 23
PYTHON SETUP FOR AILITE ​

## Slide 24
​
PREREQUISITES NEED TO BE INSTALLED :​
    Visual Studio Code​
    Python (Preferable Version : 3.11.10)​
    Install Python interpreter inside the VS code​
    Miniconda​

## Slide 25
CREATING MINICONDA ENVIRONMENT & REQUIREMENTS INSTALLATION:​
​Steps to Set Up and Run the Python Program:
Create a Conda Environment:
Open Miniconda and create an environment with Python 3.11 in the desired file path:
conda create -n <environment-name> python=3.11 -y
Activate the Environment:
Activate the newly created environment:
conda activate <environment-name>
Install Required Packages:
Install all necessary Python packages from the requirements file:
pip install -r requirements.txt
Run the Program:
Execute the Python script:
python <file_name.py>

## Slide 26
PYTHON PROJECTS​

## Slide 27
OBJECT DETECTION:​
Goal: Detect and recognize traffic signs using YOLO (You Only Look Once) object detection.​
Functionality: Control the bot based on the detected traffic sign.​
Movement Capabilities: The bot can move forward, backward, left, and right​
Key Components:​
YOLO Object Detection:​
  Real-time detection of traffic signs.​
  Accurate and fast recognition using YOLO algorithm.
  Bot Actions:​
  Executes specific movements in response to recognized traffic signs.​
  Example actions: Forward ,Backward, Left, Right

## Slide 28
TEXT RECOGNITION:​
Goal: Utilize EASYOCR (Optical Character Recognition) to detect text from a webcam feed and control a robotic bot accordingly.​
Functionality: Recognizes commands such as "GO", "LEFT", "RIGHT", and "STOP", then sends corresponding signals to a specified IP address to control the bot.​
Key Components:​
OCR Technology:​
  Easy OCR: Used for accurate and efficient text recognition from the webcam feed.​
Real-time Processing:​
  Integrates with the webcam to provide continuous text detection .​
Bot Actions:​
  Executes specific movements in response to recognized Letter.​

## Slide 29
HAND GESTURE RECOGNITION:​
Goal: Perform hand gesture recognition using Media pipe and control a robotic bot accordingly.​
Functionality: Detects various hand gestures in real-time and sends corresponding commands to a specified host.​
Key Components:​
Media pipe Library:​
  Utilizes advanced machine learning models for accurate hand gesture detection.​
Real-time Processing:​
  Integrates with a webcam to capture and analyze hand gestures continuously.​
Bot Actions Based on Gestures:​
Recognizes predefined hand gestures.​
Software Requirements: Media pipe, OpenCV

## Slide 30
FACE RECOGNITION:​
Goal: Perform face recognition using the Deep Face library and grant access based on recognized faces.​
Functionality: Detects faces in real-time and compares them with reference images. If a match is found, access is granted and commands can be triggered via keyboard inputs.​
Key Components:​
Deep Face Library: Utilizes state-of-the-art facial recognition models. Compares captured faces with pre-stored reference images.​
Real-time Processing:​
Integrates with a webcam for continuous face detection and recognition.​
Bot Actions:​
Upon recognizing a face, access is granted.​
Software Requirements: Deep Face, OpenCV

## Slide 31
Charging the AI-Lite Kit
The Kit uses a 3.7V Li-ion cell for powering. Kindly be aware that the kit must be charged only in OFF state. Use a 5V (voltage) adapter for charging. You can use either a wall adapter, phone charger, or laptop port exclusively for charging.
Given below are indications near Type-C charging port:
When the Kit is connected to charger in OFF state, the LED will indicate Red.
When the Kit is fully charged, the LED will indicate Green.
Caution: Do not charge the kit in ON state mode

## Slide 32
GITHUB Link to Download the codes
The AI-Lite Kit uses the repository that can be downloaded by scanning this QR code.
Figure - 8
Figure - 7​
MIT Applications
Python Applications

## Slide 33
For support email us at support@meritus.ai